LTFSArchiver 1.0 Configuration and Administration

Summary

This document describes in detail the configuration of the system and its management. It is explained for example how to start and end the system service (ltfsarchiver) and how to keep track of what is going on through log files.

Configuration file(s)

The main configuration file of LTFSArchiver is:

/opt/ltfsarchiver/conf/ltfsarchiver.conf

The config file has four sections:

## Section 1: Operating mode
LTFSARCHIVER_MODE
This parameter sets the operating mode used by LTFSArchiver, accepted values are:

“B”: this corresponds to the Mixed mode, LTFSArchiver will hence use both internal (library managed) and external (manually managed) LTO tape devices.

Effects: Each archive request will be evaluated to verify if an existing internal tape (loaded into a managed library) can be used to write the data on it. If a tape is found, the request will be queued in “library mode”.
If no internal tape can be used, the system will try to find an external usable one (a tape not loaded into a library but known). If such a tape is found, the request will be queued in “manual mode”.
If also this search fails, the request will be refused (fallout status).

“C”: LTFSArchiver will use only internal (library managed) LTO tape devices.
Effects: Each archive request will be evaluated to verify if an existing internal tape can be used to write the data on it. If a tape is found, the request will be queued in “library mode”.
If no internal tape can be used, the request will be refused (fallout status).

“M”: LTFSArchiver will use only external (manually managed) LTO tape devices.
Effects: Each archive request will be evaluated to verify if an existing external tape can be used to write the data on it. If a tape is found, the request will be queued in “manual mode”. If no external tape can be used, the request will be refused (fallout status).

Default:
LTFSARCHIVER_MODE="M"

HW_CHANGER_TYPE
Used to set the type of external library used.
For now the only accepted value is “MSL”, standing for HP MSL-xxxx tape libraries.
In the future it's expected to extend support to other libraries.

Default:
HW_CHANGER_TYPE="MSL"

CHANGER_ADDRESSES (Not yet implemented)

Array containing the URLs of the administrator web interface for MSL libraries.
If more than one library is used, a blank must be used as a separator.
Useful only if the library(ies) will be network connected.

Default:
CHANGER_ADDRESSES=( http://198.162.0.2 )

HW_TAPE_TYPE
Used to set the type of tape device used.
The only accepted value is “LTO”, that supports LTO5 and LTO6 devices.
This is done for possible future use with other tape types.

Deafult:
HW_TAPE_TYPE="LTO"

## Section 2: Runtime parameters and variables section

LTFSARCHIVER_TITLE and LTFSARCHIVER_VERSION
These strings are shown on the web interface to present the tool.

default:
LTFSARCHIVER_TITLE="LTFS Archiver"
LTFSARCHIVER_VERSION="1.3.subversion"

LTFSARCHIVER_HOME and LTFSARCHIVER_LOGDIR
These are the paths to home and log directories

default:
LTFSARCHVER_HOME=”_LTFSARCHIVER_HOME_” (*)
LTFSARCHIVER_LOGDIR="$LTFSARCHIVER_HOME/logs"

(*) NB: it's a placeholder that will be overwritten by install script

LTFSARCHIVER_LOGLEVEL and LTFSARCHIVER_DEBUG
LTFSARCHIVER_LOGLEVEL is used to set the verbosity of the log (0=minimum, 4=maximum)
If LTFSARCHIVER_DEBUG is set to “1”, the log strings (those that have to be printed according to LTFSARCHIVER_LOGLEVEL value) will be also sent to standard output (useful when manually launching LTFSArchiver as a script, instead of service)

default:
LTFSARCHIVER_LOGLEVEL=1
LTFSARCHIVER_DEBUG=0

LTFSARCHIVER_USER, LTFSARCHIVER_GROUP and LTFSARCHIVER_DB
The first two parameters define the user name and group used as UID and GID during the ltfs mount procedure.
The LTFSARCHIVER_USER has also to be the owner of the database used by LTFSArchiver, whose name has to be set through the LTFSARCHIVER_DB variable

default:
LTFSARCHIVER_USER="pprime"
LTFSARCHIVER_GROUP="pprime"
LTFSARCHIVER_DB="ltfsarchiver"

LTFSARCHIVER_LTFSTIMEOUT
Is the time in seconds LTFSArchiver has to wait after ltfs' unmount command (if mount issued in RW mode) before considering succesfully completed the eject/recovery tape.
After an umount command, in fact, ltfs needs some time to physically update the index partition. Removing the tape before the index update (even if physically allowed by the device) may cause a filesystem corruption(see also LTFSARCHIVER_LTFSSYNC parameter)
This parameter is ignored when unmountig a R/O ltfs. Please be careful when considering to lower the default that is set to 120 seconds.

Default:
LTFSARCHIVER_LTFSTIMEOUT=120

LTFSARCHIVER_MAXRESTORE_PRIORITY
Reserved for future uses, it is intended to set a priority rate between restore and other requests.

Default:
LTFSARCHIVER_MAXRESTORE_PRIORITY=0

LTFSARCHIVER_INTERRUN
It is the number of seconds between each agent run. Lower values assure more promptness of the system but also a higher overhead.

Default:
LTFSARCHIVER_INTERRUN=60

LTFSARCHIVER_LTFSSYNC
Determines the mode ltfs will executes the sync of the index partition (see also LTFSARCHIVER_LTFSTIMEOUT parameter). Used only when the LTO Tape is mounted in R/W. Accepted values are the same accepted by the system command ltfs mount: time, close, unmount.
The unmount mode is preferred (the default) because if the archive procedure has to write a lot of files, time and close modalities can cause frequent index updates and consequent long rewind/update/fast forward operations).
Using unmount instead, the index update will be executed only once per run.

Default:
LTFSARCHIVER_LTFSSYNC="unmount"

LTFSARCHIVER_RULESIZE and LTFSARCHIVER_RULEEXTS
Set these variable to determine the files that should be stored into the “a” (or index) partition of a LTO5/LTFS tape.

LTFSARCHIVER_RULESIZE sets the maximum filesize amount a file can have to be stored in the index partition

LTFSARCHIVER_ RULEEXTS array sets the extension(s) of the files that will be stored in the index partition
Please note that BOTH conditions have to be satisfied to allow the file being stored in the index partition.

Sample:
LTFSARCHIVER_RULESIZE="2M"
LTFSARCHIVER_RULEEXTS=( txt htm html )

This ruleset will cause storing into the index partition the “*txt”, “*htm” and “*html” files if they are smaller than 2 MB.
Files with other extensions OR bigger than 2 MB will be stored into the data partition

Default:
LTFSARCHIVER_RULESIZE="5M"
LTFSARCHIVER_RULEEXTS=( txt xml jpg )

Caveat:
The same criteria will be applied during a directory archiving process to optimize the performance of the process itself.
Changing them after having formatted one o more tape may lead to slow archive operations as archive process will use different values than the ones used by ltfs.

LTFSARCHIVER_RULEOVER (not implemented yet)
If set to (Y)es mkltfs will format tape allowing a future override of formatting rules.
If set to (N)o mkltfs will format tape without allowing future override.
For future use

Default:
LTFSARCHIVER_RULEOVER="n"

LTFSARCHIVER_MAXAVAIL
Max concurrent active instances of makeavailable requests.
When a tape is loaded due to a “makeavailable” request, it will lock both the tape and the drive device during the time it stays online. If you have more than one LTO driver, you can set this parameter to a smaller number, in order to avoid blocking other queued tasks.

Default:
LTFSARCHIVER_MAXAVAIL=2

LTFSARCHIVER_MNTAVAIL
Is the “base” mountpoint where the makeavailable access point will be created e.g., if the tape “EX000000” is made available, its mount point will be:
$LTFSARCHIVER_MNTAVAIL/EX000000

Default:
LTFSARCHIVER_MNTAVAIL="/mnt/ltfsarchiver/lto-ltfs"

LTFSARCHIVER_LOCK_LABEL
A sort of “dummy label” used to put a tape device in unusable status through the web interface (see “LTFSArchiverWebGUI”).
An attempt to use Tapemanager/Add command to add a tape with this label will be refused.

Default:
LTFSARCHIVER_LOCK_LABEL="donotuse"

LTFSARCHIVER_DAYSKEEP
Sets the “time to live” (in days) of logfiles and db entries.
A batch (located in /etc/cron.daily) proveds removing from db the records pertaining to instances succesfully completed (failed ones are NOT removed) and logfiles if older the the number of days specified.
Set this parameter according to your needs.

Default:
LTFSARCHIVER_DAYSKEEP=10

GUESSED_CONF
It's the name of the auto-configuration file generated by the script
/opt/pprime/sbin/utils/guess_conf.sh (see further).

Default:
GUESSED_CONF=$LTFSARCHIVER_HOME/conf/guessed.conf

LTFSARCHIVER_OUTPUT
Sets the default output format for API'S calls.
Available values are “XML” and “JSON”
This format can be overridden adding “Output=format” while calling API'S

Default:
LTFSARCHIVER_OUTPUT=”XML”

LTFSARCHIVER_DEFPOOL
Sets the name of the deafult pool that will be used by API's when not specified using PoolName parameter.

Delfault:
LTFSARCHIVER_DEFPOOL="defaultfs"

LTFSARCHIVER_DAYSKEEP
Sets the retention period (in days) for tasks report files and request table entries after their completion
After this period, the daily automatic cleaner batch will remove files from report directory and from internal DB.

Deafult:
LTFSARCHIVER_DAYSKEEP=100

LTFSARCHIVER_NAMESPACE
Sets the namespaces used to validate reports

Default:
LTFSARCHIVER_NAMESPACE='xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:xlink="http://www.w3.org/1999/xlink"'

GUESSED_CONF
Sets the path to the override config file.
This file can be generated by guess_conf.sh script or manually edited by user.
Please see Section 4 for the type and list of parameters usally managed by this file

Default:
GUESSED_CONF=$LTFSARCHIVER_HOME/conf/guessed.conf

LTO_ALLOWED_CODES and LTO_ALLOWED_TYPES
These arrays (they must be set as arrays even if you want to configure LTFSArchiver to allow a single LTO type) contains the Density Code(s) that identify the different LTO types and their well-known names.
Of course, the nth density code of the first array must match with the nth LTO type.

Default:
LTO_ALLOWED_CODES=( 0x58 0x5a )
LTO_ALLOWED_TYPES=( LTO5 LTO6 )

LTO_WATERMARK
This array must have the same number of elements as the previous two.
Each element represents the minimum available space (in MB) for a tape (according to his known type) to be considered available for a new archive request. This is done because ltfs does not allow to fill a tape more than 98-99% of its declared capacity. If a LTO5 tape has less than about 22 GB of free space, the tape will be mounted in R/O mode even if R/W was specified.

Default:
LTO_WATERMARK=( 22000 33000 )

## Section 3: Paths to command and db access
It includes the major paths to the OS commands used for the core activities.
This section should not be modified, except if a non-default version of a command or utility has to be used.

PATH=/usr/local/bin:$PATH (*)
CMD_MTX=`which mtx`
CMD_MT=`which mt`
CMD_PSQL=`which psql`
CMD_LTFS=`which ltfs`
CMD_MD5=`which md5sum`
CMD_SHA1=`which sha1sum`
CMD_MKLTFS=`which mkltfs`
CMD_XMLLINT=`which xmllint`
CMD_RSYNC=`which rsync`" -vas"
CMD_XSL=`which xsltproc`
CMD_DB="$CMD_PSQL -U $LTFSARCHIVER_USER -d $LTFSARCHIVER_DB -t -c "
CMD_DB_HTML="$CMD_PSQL -U $LTFSARCHIVER_USER -d $LTFSARCHIVER_DB -H -c "

(*) /usr/local/bin is the path where usually LTFS's binary binaries are installed; if this path is not set for root shell, they could be unavailable

## Section 4: Library and tape devices (see usage of guess_config further)

CONF_CHANGER_DEVICES
String array containing the physical device name(s) of the used library(ies), a blank must be used as a separator.
Sample of a system with two libraries with device name sg5 and sg8:
CONF_CHANGER_DEVICES=( /dev/sg5 /dev/sg8 )

Default:
CONF_CHANGER_DEVICES=( /dev/sg5 )

CONF_CHANGER_SLOTS
String array containing the number of slot (Storage Element) available for each library.
A blank must be used as a separator.
The order must be the same used for libraries with the CHANGER_DEVICES array.
Referring to previous sample, and supposing that sg5 library has 24 slot and sg8 has 48 slots, the array must be:
CONF_CHANGER_SLOTS=( 24 48 )

Default:
CONF_CHANGER_SLOTS=( 24 )

CONF_CHANGER_TAPES
Array containing the number of tape devices (Data Transfer Element) available for each library. A blank must be used as a separator.
The order must be the same used for libraries with the CHANGER_DEVICES array.
Referring to previous sample and supposing that sg5 library has 2 tapes and sg8 has 1 tape, the array must be:
CONF_CHANGER_TAPES=( 2 1 )

Deafult:
CONF_CHANGER_TAPES=( 1 )

CONF_CHANGER_TAPEDEV_X (where x= 0, 1... n)
Array containing the device address(es) of the tape devices associated to library X (where X is the zero-based index of the library array CHANGER_DEVICES).
A blank must be used as a separator.
Referring to previous sample and supposing that sg5 library has two tape drives st6 and st7 and sg8 library has a single tape st9, the arrays must appear as:

CONF_CHANGER_TAPEDEV_0=( /dev/st6 /dev/st7 )
CONF_CHANGER_TAPEDEV_1=( /dev/st9 )

Default
CONF_CHANGER_TAPEDEV_0=( /dev/st0 )

CONF_MANUAL_TAPEDEV
Is the array containing the device addresse(s) of ALL external tape device connected to the LTFSarchiver system.
A blank must be used as a separator.

Sample:
CONF_MANUAL_TAPEDEV=( /dev/st2 /dev/st3 )

Default:
CONF_MANUAL_TAPEDEV =( /dev/st1 )

CONF_BACKEND
Array containing informations about the backend emulator that will be used by LTFS commands.
As different LTFS builds use different backend and device default values, a correct setting of this array will allow LTFSArchiver to manage in the correct way tape devices coming from different vendors.
The array data are stored in the form “scsi-tapedevice-address” “backend-value”
See Appendix B for a deeper discussion about backend and device name.

Sample:
CONF_BACKENDS=( /dev/st0 ibmtape /dev/st1 ltotape /dev/st2 orcltape)

Default :
CONF_BACKENDS=( /dev/st0 ltotape /dev/st1 ltotape )

## Guessed_config file
Trying to make simpler the parameters set up in section 4 of the configuration file, it is possible to execute a script based on the sg_map system utility; please ensure that sg_map package has been installed or the script will fail.

Launching the script.

Login as root user and run: $LTFSARCHIVER_HOME/sbin/utils/guess_conf.sh

Each time the script finds a device that announce itself as a library or as a tape, a message will be printed. An example follows:

Step 1: Tape changers
Tape loader(s) found: 1
scsi device /dev/sg6 appears to be a library
Step 2: Tape devices
Tape device(s) found: 2
Step 3: Changers/Tape associations
scsi device /dev/st1 appears to be a tape owned by /dev/sg6 library
Step 4: Standalone tapes
scsi device /dev/st0 appears to be an external tape

Finally, the guessed configuration found will be compared with the existing (if existing...) guessed configuration file (see GUESSED_CONF variable) and shown:

The guessed conf doesn't differ from running conf:
--------------------------------------------------
CONF_BACKENDS=( /dev/st0 ltotape /dev/st1 ltotape )
CONF_CHANGER_DEVICES=( /dev/sg6 )
CONF_CHANGER_SLOTS=( 48 )
CONF_CHANGER_TAPEDEV_0=( /dev/st1 )
CONF_CHANGER_TAPES=( 2 )
CONF_MANUAL_TAPEDEV=( /dev/st0 )
--------------------------------------------------

Updating the configuration

If the guessed conf file doesn't exist or differs from active configuration, the user is asked whether to update the configuration or not. Answering “Y”, the old GUESSED_CONF file will be overwritten by the new one. Please refer to Appendix A for more information and cautions about configuration guessing.

Starting/stopping service
Actually the real actions (e.g. read/write operations) are performed by a unique system service called ltfsarchiver that works by carrying out jobs queued on the database.
The service should be configured to be started at runlevels 3 and 5, using 90 as start priority (or, at least, at a lower priority than postgresql and apache daemons)

## Status
To check the status of the agent, supply use the command:

service lftsarchiver status

Possible answers are:

ltfsarchiver is running
ltfsarchiver is stopped
[WARNING] ltfsarchiver (RUNPID) is running, but pidfile is missing.
[WARNING] ltfsarchiver not running, but pidfile (FOUNDPID) exixts

RUNPID is the process id (PID) of the running instance.
FOUNDPID is the process id (PID) found into the pidfile.

## Start
To start the agent, supply the command:

service lftsarchiver start

Start will be actually attempted only if no other instance is currently running AND pidfile doesn't exists.

Possible answers are:

ltfsarchiver started
ltfsarchiver (RUNPID) is already running
[WARNING] ltfsarchiver not running, but pidfile (FOUNDPID) exixts
[WARNING] ltfsarchiver (RUNPID ) is running, but pidfile is missing

## Stop
To stop the agent, supply the command:

service lftsarchiver stop

Stop will be actually attempted only if an instance is currently running AND pidfile matches the one of the running instance.

possible answers are:

ltfsarchiver stopped
ltfsarchiver already stopped
[WARNING] ltfsarchiver not running, but pidfile exists... removing
[WARNING] Running process pid (RUNPID) didn't match pidfile (FOUNDPID)
[WARNING] ltfsarchiver (RUNPID ) is running, but pidfile is missing

Please note that stopping the agent will NOT break currently active requests, but simply prevents LTFSArchiver from trying to satisfy further requests. The requests in wait status at the moment of the switch off are not lost but executed when the service will be started again.
This means that a tape which has been put in “available online” status will be left mounted if a umount command has been issued but still not executed at stop time.

Log files
LTFSArchiver logs its activities using several files, all of them are placed in the directory specified with the LTFSARCHIVER_LOGDIR parameter.

The main logfile has the following name:

ltfsarchiver.YYYYMMDD.log

where YYYYMMDD is the date when tape_agent started.
It reports if new incoming requests are found and if they are going to be processed or not (and the reason in the last case).

When a request is processed the corresponding activity is reported in a separate log file named:

tape_agent_ssssssssss.log

where ssssssssss is the time when tape agent started in “seconds since 1970/01/01”

The log level is determined by the parameter LTFSARCHIVER_LOGLEVEL
Appendix A – Guessed configuration

Take care that the result of the guess_conf script may, in some cases, lead to wrong configurations.
As an example, an HP MSL4048 with two tape drives appears to be a tape library with a single drive, while the second tape will be detected as an external one.
This happens because the arm is accessible through the same FC bus assigned to the first OR the second tape device.

Here follows a real sample of the guess_config output obtained with the guessing utility on a server with an HP MSL 4048 with two LTO drives (/dev/st0 and /dev/st1) and an external HP desktop LTO drive (/dev/st2).

CONF_CHANGER_TAPEDEV_0=( /dev/st0 )
CONF_CHANGER_DEVICES=( /dev/sg6 )
CONF_CHANGER_SLOTS=( 48 )
CONF_CHANGER_TAPES=( 2 )
CONF_MANUAL_TAPEDEV=( /dev/st1 /dev/st2 )

While the right configuration should be:
CONF_BACKENDS=( /dev/st0 ltotape /dev/st1 ltotape /dev/st2 ltotape )
CONF_CHANGER_TAPEDEV_0=( /dev/st0 /dev/st1 )
CONF_CHANGER_DEVICES=( /dev/sg6 )
CONF_CHANGER_SLOTS=( 48 )
CONF_CHANGER_TAPES=( 2 )
CONF_MANUAL_TAPEDEV=( /dev/st2 )

When the script should detect that the number of tape devices associated to a media changer is lower that the value declared by the changer itself, a warning message will be displayed:

!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
WARNING!
Changer /dev/sg6 has 2 tape device(s),
but the guessed conf script detected 1 tape device(s)
maybe one of the following device(s) are actually managed by /dev/sg6
--> /dev/st1
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

Consider the guess_conf script as an aid to configure the system, not as an error proof tool.

Appendix B – LTFS devname and backend

According to LTFS documentation, LTFS needs to know “who” and “how” to interact with a tape device.
“who” is the devname: it a remap from generic /dev/sgX (i.e. /dev/stX)
“how” is the backend: the manufacturer’s specific driver library (i.e. ltotape)

Several manufacturer have released their own LTFS version, each of them using different default values for these parameters.

Additionally, IBM uses a different device naming (/dev/IBMtapeX instead of /dev/stX), and a specific package (lin_tape) is needed to create the correct device name.
The default devname and backend values used by some LTFS distribution are reported:

Distribution	Devname	Backend
HP	/dev/stX	ltotape
IBM	/dev/IBMtapeX	ibmtape
Oracle	/dev/stX	orcltape
Quantum	/dev/stX	ltotape

The guess_config script tries to get the tape vendor name through an “tapeinfo” call and finally create the CONF_BACKENDS array according to the values returned.

Appendix C - Compatibility tests

In order to have LTFSArchiver correctly working with different tape device, media changers and LTFS “flavors”, it has been tested with the following:

## LTFS Versions

Distribution	LTFS version	Index Spec. Version	Note
HP	1.2.2	2.0.0	No support for orcltape
	2.0.0	2.0.0
IBM	1.3.0	2.0.1	No support for ltotape/orcltape
Oracle	1.2.0	2.0.0
Quantum	2.0.0	2.0.0	No support for orcltape

## LTO Tape devices

Manifacturer	Model / (reported from tapeinfo)	Revision	Conn.	Notes
HP	Ultrium 5-SCSI	I3BW	FC	Internal - MSL G3 Series
HP	Ultrium 5-SCSI	Z3ED	SAS	Desktop model
IBM	ULT3580-HH5	BBNF	SAS	Desktop model

## Media changers

Manifacturer	Model / (reported from tapeinfo)	Revision	Conn.	Notes
HP	MSL G3 Series	5.00	FC	MSL 2024 (1 drive)
HP	MSL G3 Series	8.10	FC	MSL 4048 (2 drives)